## Slide 1
Chapter 8
Switching
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: 1

## Slide 2
Chapter 8: Outline
8.1 INTRODUCTION
8.2 CIRCUIT-SWITCHED NETWORK
8.3 PACKET-SWITCHING
8.4 STRUCTURE OF A SWITCH
Notes: 8.#

## Slide 3
Chapter 8: Objective
The first section introduces switching. It mentions three methods of switching: circuit switching, packet switching, and message switching. The section then defines the switching methods that can occur in some layers of the Internet model.
The second section discusses circuit-switched networks. It first defines three phases in these types of networks. It then describes the efficiency and delay of these networks.
The third section briefly discusses packet-switched networks. It first describes datagram networks. The section then describes virtual circuit networks.
The last section discusses the structure of a switch. It first describes the structure of a circuit switch. It then explains the structure of a packet switch.
Notes: 8.#

## Slide 4
8.4
    8-1 INTRODUCTION
A network is a set of connected devices. Whenever we have multiple devices, we have the problem of how to connect them to make one-to-one communication possible. The solution is switching. A switched network consists of a series of interlinked nodes, called switches.
Notes: 8.#

## Slide 5
8.5
Figure 8.1: Switched network
These are switches jab connection ban jata h to ye next switch
ka address contain kar late h path remember karne k lyea
Notes: 8.#

## Slide 6
8.6
8.8.1 Three Methods of Switching
Traditionally, three methods of switching have been discussed: circuit switching, packet switching, and message switching. The first two are commonly used today. The third has been phased out in general communications but still has applications. Packet switching can further be divided into two subcategories, virtual-circuit approach and datagram approach, as shown in Figure 8.2.
Notes: 8.#

## Slide 7
8.7
8.8.2 Switching and TCP/IP Layers
Switching can happen at several layers of the TCP/IP protocol suite: at the physical layer, at the data-link layer, and at the network layer.
Notes: 8.#

## Slide 8
8.8
Figure 8.2: Taxonomy of switched networks
Notes: 8.#

## Slide 9
8.9
    8-2 CIRCUIT-SWITCHED NETWORKS
A circuit-switched network consists of a set of switches connected by physical links. A connection between two stations is a dedicated path made of one or more links. However, each connection uses only one dedicated channel on each link. Each link is normally divided into n channels by using FDM or TDM, as discussed in Chapter 6.
Notes: 8.#

## Slide 10
8.10
Figure 8.3: A trivial circuit-switched network
Notes: 8.#

## Slide 11
As a trivial example, let us use a circuit-switched network to connect eight telephones in a small area. Communication is through 4-kHz voice channels. We assume that each link uses FDM to connect a maximum of two voice channels. The bandwidth of each link is then 8 kHz. Figure 8.4 shows the situation. Telephone 1 is connected to telephone 7; 2 to 5; 3 to 8; and 4 to 6. Of course the situation may change when new connections are made. The switch controls the connections.
Example 8.1
8.11
Notes: 11

## Slide 12
As another example, consider a circuit-switched network that connects computers in two remote offices of a private company. The offices are connected using a T-1 line leased from a communication service provider. There are two 4 × 8 (4 inputs and 8 outputs) switches in this network. For each switch, four output ports are folded into the input ports to allow communication between computers in the same office. Four other output ports allow communication between the two offices. Figure 8.5 shows the situation.
Example 8.2
8.12
Notes: 12

## Slide 13
8.13
Figure 8.4: Circuit-switched network used in Example 8.1
Notes: 8.#

## Slide 14
8.14
8.2.1 Three Phases
The actual communication in a circuit-switched network requires three phases: connection setup, data transfer, and connection teardown.
Notes: 8.#

## Slide 15
8.15
Figure 8.5: Circuit-switched network used in Example 8.2
Notes: 8.#

## Slide 16
8.16
8.2.2 Efficiency
It can be argued that circuit-switched networks are not as efficient as the other two types of networks because resources are allocated during the entire duration of the connection. These resources are unavailable to other connections. In a telephone network, people normally terminate the communication when they have finished their conversation.
Notes: 8.#

## Slide 17
8.17
8.2.3 Delay
Although a circuit-switched network normally has low efficiency, the delay in this type of network is minimal. During data transfer the data are not delayed at each switch; the resources are allocated for the duration of the connection. Figure 8.6 shows the idea of delay in a circuit-switched network when only two switches are involved.
Notes: 8.#

## Slide 18
8.18
Figure 8.6: Delay in a circuit-switched network
Notes: 8.#

## Slide 19
8.19
    8-3 PACKET SWITCHING
In data communications, we need to send messages from one end system to another. If the message is going to pass through a packet-switched network, it needs to be divided into packets of fixed or variable size. The size of the packet is determined by the network and the governing protocol.
Notes: 8.#

## Slide 20
8.20
8.3.1 Datagram Networks
In a datagram network, each packet is treated independently of all others. Even if a packet is part of a multipacket transmission, the network treats it as though it existed alone. Packets in this approach are referred to as datagrams.
Notes: 8.#

## Slide 21
8.21
Figure 8.7: A Datagram network with four switches (routers)
Notes: 8.#

## Slide 22
8.22
Figure 8.8: Routing table in a datagram network
Notes: 8.#

## Slide 23
8.23
Figure 8.9: Delays in a datagram network
Notes: 8.#

## Slide 24
8.24
8.3.2 Virtual-Circuit Networks
A virtual-circuit network is a cross between a circuit-switched network and a datagram network. It has some characteristics of both.
Notes: 8.#

## Slide 25
8.25
Figure 8.10: Virtual-circuit network
Notes: 8.#

## Slide 26
8.26
Figure 8.11: Virtual-circuit identifier
Notes: 8.#

## Slide 27
8.27
Figure 8.12: Switch and table for a virtual-circuit network
VCI:- it uniquely identify the virtual circuit within the network
Notes: 8.#

## Slide 28
8.28
Figure 8.13: Source-to-destination data transfer in a circuit-switch network
Notes: 8.#

## Slide 29
8.29
Figure 8.14: Setup request in a virtual-circuit network
Notes: 8.#

## Slide 30
8.30
Figure 8.15: Setup acknowledgment in a virtual-circuit network
Notes: 8.#

## Slide 31
8.31
Figure 8.16: Delay in a virtual-circuit network
Notes: 8.#

## Slide 32
8.32
    8-4 STRUCTURE OF A SWITCH
We use switches in circuit-switched and packet-switched networks. In this section, we discuss the structures of the switches used in each type of network.
Notes: 8.#

## Slide 33
8.33
8.4.1 Structure of Circuit Switches
Circuit switching today can use either of two technologies: the space-division switch or the time-division switch.
Notes: 8.#

## Slide 34
8.34
Figure 8.17: Crossbar switch with three inputs and four outputs
Notes: 8.#

## Slide 35
8.35
Figure 8.18: Multistage switch
Notes: 8.#

## Slide 36
To design a three-stage switch, we follow these steps:
1. We divide the N input lines into groups, each of n lines. For each group, we use one crossbar of size n × k, where k is the number of crossbars in the middle stage. In other words, the first stage has N/n crossbars of n × k crosspoints.
2. We use k crossbars, each of size (N/n) × (N/n) in the middle stage.
3. We use N/n crossbars, each of size k × n at the third stage.

## Slide 37
Design a three-stage, 200 × 200 switch (N = 200) with k = 4 and n = 20.
Solution
In the first stage we have N/n or 10 crossbars, each of size 20 × 4. In the second stage, we have 4 crossbars, each of size 10 × 10. In the third stage, we have 10 crossbars, each of size 4 × 20. The total number of crosspoints is 2kN + k(N/n)2, or 2000
crosspoints. This is 5 percent of the number of crosspoints in a single-stage switch (200 × 200 = 40,000).
Example 8.3
8.37
Notes: 37

## Slide 38
Redesign the previous three-stage, 200 × 200 switch, using the Close criteria with a minimum number of crosspoints.
Solution
We let n = (200/2)1/2, or n = 10. We calculate k = 2n – 1 = 19. In the first stage, we have 200/10, or 20, crossbars, each with 10 × 19 crosspoints. In the second stage, we have 19 crossbars, each with 10 × 10 crosspoints. In the third stage, we have 20 crossbars each with 19 × 10 crosspoints. The total number of crosspoints is 20(10 × 19) + 19(10 × 10) + 20(19 × 10) = 9500. If we use a single-stage switch, we need 200 × 200 = 40,000 crosspoints. The number of crosspoints in this switch is 24 percent that of a single-stage switch.
Example 8.4
8.38
Notes: 38

## Slide 39
8.39
Figure 8.19: Time-slot interchange
Notes: 8.#

## Slide 40
8.40
Figure 8.20: Time-space-time switch
Notes: 8.#

## Slide 41
8.41
8.4.2 Structure of Packet Switches
A switch used in a packet-switched network has a different structure from a switch used in a circuit-switched network. We can say that a packet switch has four components: input ports, output ports, the routing processor, and the switching fabric, as shown in Figure 8.28.
Notes: 8.#

## Slide 42
8.42
Figure 8.21: Packet switch components
Notes: 8.#

## Slide 43
8.43
Figure 8.22: Input port
Notes: 8.#

## Slide 44
8.44
Figure 8.23: Output port
Notes: 8.#

## Slide 45
8.45
Figure 8.24: A banyan switch
Notes: 8.#

## Slide 46
8.46
Figure 8.25: Example of routing in a banyan switch (Part a)
Notes: 8.#

## Slide 47
8.47
Figure 8.25: Example of routing in a banyan switch (Part b)
Notes: 8.#

## Slide 48
8.48
Figure 8.26: Batcher-banyan switch
Notes: 8.#