## Slide 1: Combinational Circuits

## Slide 2: Circuits
Combinational Circuit:
output of this circuit mainly depends on the input terminals at any time.
n binary input variables come and m binary output variables go out.
This circuit doesn’t include any memory.

## Slide 3: Adder
An adder is a digital logic circuit that is used for the addition of numbers.
Adders are basically classified into two types:
Half-Adder
Full-Adder.

## Slide 4: Half-Adder
Half Adder performs the arithmetic addition of two bits.
The half adder accepts two binary digits on its inputs and produce two binary digits outputs, sum (S) and carry (C) bit.
The carry (C) output is 0 unless both the inputs are 1.
S represents the least significant bit of the sum.

## Slide 5: Half-Adder
Logical Expression of Half-Adder:
Sum (S) = AB + AB = A  B
Carry (C) = A B = A AND B
A | B | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Table: Truth Table
Fig: Block diagram of Half-Adder

## Slide 6: Half-Adder
Logical Expression of Half-Adder:
Sum (S) = AB + AB = A  B
Carry (C) = A B = A AND B
A | B | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Table: Truth Table
Fig: Logic diagram of Half-Adder

## Slide 7: Full-Adder
Full Adder performs the arithmetic sum of three bits.
The Full-Adder accepts three inputs and produce two outputs.
The S output is equal to 1 when only one input is equal to 1 or when all three inputs are equal to 1.
The C output has carry of 1 if two or three inputs are equal to 1.

## Slide 8: Full-Adder
Logical Expression of Full-Adder:
Sum (S) = ABCin + AB Cin  AB Cin + ABCin = A  B  Cin
Carry (Cout) = A B +A Cin + B Cin
Table: Truth Table
Fig: Block diagram of Full-Adder
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 9: Full-Adder
Logical Expression of Full-Adder:
Sum (S) = ABCin + AB Cin  AB Cin + ABCin = A  B  Cin
Carry(Cout)=AB+ACin+BCin=A B+(AB+AB)Cin
Table: Truth Table
Fig: Logic diagram of Full-Adder
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
=A B+(A  B )Cin

## Slide 10: Subtractor
Subtractor: each subtrahend bit of the number is subtracted from its corresponding significant minuend bit to form a difference bit.
If the minuend bit is smaller than the subtrahend bit, a 1 is borrowed from the next significant position.
Half-Subtractor
Full-Subtractor.

## Slide 11: Half-Subtractor
A half-subtractor is a circuit that subtracts two bits and produces their difference.
The half-subtractor needs two outputs.
One output generates the difference (D).
The second output for borrow (B).
To perform x-y, we have to check the relative magnitudes of x and y. If x>= y, we have three possibilities:
0-0=0, 1-0=1 and 1-1=0.
If x<y, we have 0-1 and it is necessary to borrow a 1 from the next higher stage.

## Slide 12: Half- Subtractor
Logical Expression of Half-Subtractor:
Difference (D) = xy + xy = A  B
Borrow (B) = xy = x AND y
x | y | B | D
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
Table: Truth Table
Fig: Block diagram of Half-Subtractor

## Slide 13: Half- Subtractor
Logical Expression of Half-Subtractor:
Difference (D) = xy + xy = A  B
Borrow (B) = xy = x AND y
x | y | B | D
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
Table: Truth Table
Fig: Logic diagram of Half-Subtractor

## Slide 14: Full-Subtractor
A Full-subtractor performs a subtraction between two bits and taking into account the borrow bit.
This circuit has three inputs and two outputs
The three inputs x, y and Bin, where Bin is previous borrow.
The two outputs, D and Bout represent the difference and output borrow, respectively.

## Slide 15: Full-Subtractor
Logical Expression of Full-Subtractor:
Difference (D) = xy Bin + xy Bin  xy Bin + xy Bin = x  y  Bin
Borrow (Bout) = x y +x Bin + y Bin
Table: Truth Table
Fig: Block diagram of Full-Subtractor
x | y | Bin | Bout | D
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 16: Full-Subtractor
Logical Expression of Full-Subtractor:
Difference (D) = xy Bin + xy Bin  xy Bin + xy Bin = x  y  Bin
Borrow (Bout) = x y+( x  y)Bin
Table: Truth Table
Fig: Logic diagram of Full-Subtractor
x | y | Bin | Bout | D
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1